Corvette Torque Specs TORQUE SPECS (Not sure if correct for all years) Ball Joint Nut, Lower 20 ft lbs Ball Joint Nut, Upper 45 ft lbs Ball Joint Service Bolts 20 ft lbs Body Mounts (all 8) 45 ft lbs Brake Caliper Anchor Bolt 75 ft lbs Cam Sprocket 20 ft lbs Camber Cam, Rear Strut 65 ft lbs Carrier, Front Support Cross Bolts 55+key ft lbs Carrier, Front Support to Cross Member 65 ft lbs Clutch Housing to Engine 30 ft lbs Clutch Pressure Plate 35 ft lbs Collar Bolts 40 ft lbs Connecting Rod 50 ft lbs Control Arm, Front, Upper Attaching Nuts 35 ft lbs Control Arm, Front, Lower Inner Pivot Nuts 50 ft lbs Control Arm, Rear, Rear Cross Shaft Bolts 135 ft lbs Control Arm, Rear, Front Cross Shaft Bolts 70 ft lbs Cover, Timing Chain 80 in lbs Cross member to Frame 25 ft lbs Cross member to Carrier 60 ft lbs Damper (Balancer) 85 ft lbs Distributor Clamp 10 Max ft lbs Flywheel to Crank 60 ft lbs Head Bolts, Sb 65 ft lbs Idler Arm Mounting Bolts 30 ft lbs Main Bearing Caps, SB 80 ft lbs Manifold, Exhaust, SB 20 ft lbs Manifold, Intake, SB 30 ft lbs Motor Mount, Front, to Chassis 30 ft lbs Motor Mount, Front, to Engine 25 ft lbs Motor Mount, Rear, to Cross Member 40 ft lbs Motor Mount, Rear, to Transmission 45 ft lbs Oil Filter Bypass Valve 80 in lbs Oil Pan Engine, All 80 in lbs Oil Pan Plug 20 ft lbs Oil Pump 65 ft lbs Pitman Arm to Control Valve 120-150 ft lbs Pitman Arm to Steering Box 42-47 ft lbs Power Steering Pump Pulley 60 ft lbs Power Steering Mounting Bolt 20 ft lbs Power Steering Mounting Nut 25 ft lbs Power Cylinder to Relay Rod 45 ft lbs Power Cylinder to Frame Bracket 25 ft lbs Rebound Bumper to Frame 20 ft lbs Shock Absorber, Front, Lower Bolt 10 ft lbs Shock Absorber, Front, Upper Nut 20 ft lbs Shock Absorber, Rear, Lower Nut 35 ft lbs Shock Absorber, Rear, Upper Nut 50 ft lbs Spark Plug 25 ft lbs Spindle, Drive, Nut 100+key ft lbs Spindle, Drive, to Axle Drive Shaft 75 ft lbs Spring Link Bolt to Torque Arm keyhole align Spring Retainer Bolts, Rear 65 ft lbs Stabilizer Bar Link Nuts 10 ft lbs Stabilizer Bar to Frame 10 ft lbs Stabilizer Shaft Bracket To Arm 120 ft lbs Stabilizer Shaft Bracket To Frame 120 ft lbs Stabilizer Shaft Link Bushings 25 ft lbs Starter Special Bolts 30-40 ft lbs Steering Box Cover 25 ft lbs Steering Box to Frame 30 ft lbs Steering Coupling Bolts 18 ft lbs Steering Coupling Clamp Bolts 30 ft lbs Steering Damper Bracket To Frame 18 ft lbs Steering Damper to Relay Rod 25 ft lbs Steering Damper to Frame Nut 30 ft lbs Steering Damper to Relay Rod 25 ft lbs Steering Wheel to Hub 25 ft lbs Strut Rod Bracket to Carrier 40-50 ft lbs Strut Rod to Spindle Support 80+key ft lbs Support, Drive Spindle, to Torque Arm 30 ft lbs Torque Arm Pivot 50+key ft lbs Transmission to Clutch Housing 50 ft lbs Universal Joint, Driveshaft and SB 15 ft lbs Universal Joint,bb Axle 25 ft lbs Valve Cover 50 in lbs Water Outlet 20 ft lbs Water Pump 30 ft lbs Wheel Bearing Nut, Front (Back 1-1.5 Flats) 12 ft lbs Wheel Stud Nuts 60 ft lbs